## Slide 1: The Thundering Herd: Amplifying Kernel Interference to Attack Response Times
Samuel Mergendahl*, Samuel Jero*, Bryan C. Ward*‡, Juliana Furgala*, Gabriel Parmer†, Richard Skowyra*
05/04/2022
DISTRIBUTION STATEMENT A. Approved for public release. Distribution is unlimited.
This material is based upon work supported by the Under Secretary of Defense for Research and Engineering under Air Force Contract No. FA8702-15-D-0001 and the National Science Foundation under Grant CPS-1837382. Any opinions, findings, conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the Department of Defense or the National Science Foundation.
© 2022 Massachusetts Institute of Technology. Delivered to the U.S. Government with Unlimited Rights, as defined in DFARS Part 252.227-7013 or 7014 (Feb 2014). Notwithstanding any copyright notice, U.S. Government rights in this work are defined by DFARS 252.227-7013 or DFARS 252.227-7014 as detailed above. Use of this work other than as specifically authorized by the U.S. Government may violate any copyrights that exist in this work.
*MIT Lincoln Laboratory, †The George Washington University, ‡Vanderbilt University
Notes: 1
1

## Slide 2: Thundering Herd Attacks
We investigate the effect of attacker-induced High-Priority Interference (HPI)
  High priority thread that executes on-behalf of a low-priority thread
We introduce Thundering Herd Attacks
  Use low priority/criticality threads to cause kernel HPI
  Targets IPC and budget management in the kernel
  Creates a system coordination dilemma
Kernel execution on-behalf of low-priority threads can delay high-criticality tasks
🛬
Could you wake
me up in 1ms?
😈
😈
😈
😈
😈
😈
😈
😈
😈
😈
😈
😈
😈
😈
😈
😈
Help us!
⏰
⏲
………….......
💤
crash
Timer fired!
https://sel4.systems/
L. M. Ruane, “Process synchronization in the UTS kernel,” Computing systems, vol. 3, no. 3, pp. 387–421, 1990.

## Slide 3: Mixed-Criticality Systems
Hard real-time (HRT) tasks
  Deadline misses can be physically catastrophic
  Imperative to maintain temporally correct execution
Temporal Isolation
  Temporal correctness of HRT tasks
  Even in the presence of low-criticality tasks
Mixed-Criticality Scheduling (MCS)
  Worst-case execution time is notoriously difficult to calculate
  Often leverage temporal budgeting mechanisms
Execution budgets can temporally isolate HRT tasks from low-criticality tasks
https://technologyandsociety.org/the-resilience-of-planes-trains-and-automobiles/
Notes: Additional Notes:
Systems = embedded systems, cyber physical systems, and safety-critical systems, etc.
Temporal Isolation is for reliability and security

## Slide 4: μ-kernels
OS services provided through user-level servers
  Liedtke’s minimality principle
Inter-Process Communication (IPC)
  Clients access servers through IPC
  Fast IPC is often synchronous
Clients access OS services through IPC in μ-kernels
μ-kernel
Device driver
File server
User App
User App
…
…
…
User-space
Kernel-space
Network stack
IPC
“A concept is tolerated inside the μ-kernel only if moving it outside the kernel would prevent the implementation of the system’s required functionality.”
-Jochen Liedtke
J. Liedtke, “On μ-kernel construction,” in 15th ACM Symposium on Operating Systems Principles (SOSP). ACM, 1995, pp. 237–250.
Client
s.send_ipc(args)
μ-kernel
Server
func(args) {
…
}
IPC
Synchronous IPC binds untrusting clients to servers
Notes: Additional Notes:
User-level servers
  Give great spatial isolation
Synchronous IPC mimics control flow of function calls
  Switching from clients to the server and back
Synchronous IPC binds untrusting clients to servers
  Scheduler invocations, budgets, priority-sorted, etc.

## Slide 5: IPC Optimization and Predictability
IPC has a long history of tension between performance and predictability
Client 1
μ-kernel
Server
IPC Endpoint
Client 2
TCB-S
TCB-C1
TCB-C2
Client n
…
TCB-Cn
…
Two main questions for predictable IPC:
Which thread’s priority?
Which thread’s budget?
Server contention
Priority ceiling
Priority inheritance
Constrained Execution
Budget-driven servers
Budget inheritance
μ-kernel
Suspended Threads
TCB-S
TCB-C1
TCB-C2
TCB-Cn
…
Difficult to engineer
Transitive inheritance
Budget-drains
Insufficient budget policy
Replenishment Policy
Both require kernel accounting!
Notes: Additional Notes:
Threads are queued not data in sel4
  No need for memory allocation on the IPC path
  But requires a queueing discipline
Server contention
  Priority ceiling
    Difficult to engineer
  Priority inheritance
    Dependency walkthroughs
Constrained Execution
  Budget-driven servers (i.e., deferable servers)
    Budget drain attacks
  Budget Inheritance
    Insufficient budget policy

## Slide 6: System Coordination Dilemma
System designers must carefully take into account various forms of system interference
Simple IPC Mechanisms
Inter-client Interference
Unconstrained Execution
Priority-Aware IPC Mechanisms
Budget Accounting Mechanisms
Unpredictable Thread Accounting
Kernel HPI
Traditional IPC
Interference
Thundering
Herd Attacks
These interference issues are nuanced and may be overlooked

## Slide 7: Our Work
We leave some details to the paper:
Other μ-kernels
IPC interference details
Introduction
seL4
Threat Model
Traditional IPC Interface
Thundering Herd Attacks
Evaluation
Attack Mitigations
Target kernel synchronous IPC and budget management mechanisms
Notes: Additional Notes:

## Slide 8: seL4
seL4 design decisions are a particular instance
Mutually exclusive kernel execution
Non-preemptible
Big kernel lock
Server contention queueing
I-PCP
Wait queues
MCS extensions
I-PCP: Immediate Priority Ceiling Protocol
https://sel4.systems/
Passive servers
Sporadic servers
Thread creation and control
SchedContext capability
TCB capability
Notes: Additional Notes:
Non-preemptible kernel is nice for verification
Passive servers
  Budget inheritance
  No priority inheritance
Sporadic servers
  Implement the budgets
  Temporal exception on budget drain

## Slide 9: Threat Model
MCS Setting
  Mix of low/high-criticality processes
  Interact with shared services
Dynamic system
  Each component is assigned resources
  Can dynamically request the creation of kernel objects
Admission control tests
  Unknown number of thread creation
  Such tests are often permissive for low-priority threads
Only a low-assurance compromise
  User-level compromised process
  μ-kernel and other shared services are uncompromised
We aim for a highly realistic threat model
Notes: Additional Notes:
Dynamic vs. static systems:
  OS patina vs. CAmkES

## Slide 10: Thundering Herd Attacks: Targeting IPC Mechanisms
The server executes on-behalf of the low-priority threads
The Thundering Herd Attacks can target kernel accounting for IPC to cause HPI
The kernel executes on-behalf of the low-priority threads
Malicious 1
μ-kernel
Server
IPC Endpoint
Malicious 2
TCB-V
TCB-M1
TCB-M2
Malicious n
…
TCB-Mn
…
Timer
Victim Client
Timer
The server will process O(n) low-priority threads before the victim
Low Attack Client 1
μ-kernel
Victim
IPC Endpoint
Low Attack Client 2
TCB-A1
TCB-A2
High Attack Client n
…
TCB-An
…
Timer
Attack Server
The kernel will O(n) sort the high-priority attacker to the front of the queue
Traditional Interference
Thundering Herd Attack
System Coordination Dilemma
Add priority sorted queues
Notes: Additional Notes:
Kernel sorts IPC queue
Attackers have no IPC with victim

## Slide 11: Thundering Herd Attacks: Targeting Budgeting Mechanisms
Our attacks can also cause kernel HPI from budget accounting
μ-kernel
Suspended Threads
TCB-A1
TCB-A2
TCB-An
…
Replenishment Policy
Attacker 1
Attacker 2
Attacker n
Victim
Timer
The kernel will O(n) sort the soonest-to-be-replenished thread to the front of the queue
…
Replenishment Queue Sorting Attack
Replenishment Wakeup Processing Attack
The kernel will process O(n) threads ready to be scheduled
Notes: Additional Notes:
Kernel sorts IPC queue
Attackers have no IPC with victim

## Slide 12: Evaluation
Main research questions:
RQ1: Does the interference grow linearly with respect to the number of threads?
RQ2: Can we quantitatively evaluate different mitigation strategies?
We contrast various forms of HPI with respect to the system coordination dilemma

## Slide 13: Evaluation Metrics and Methodology
Testbed
  seL4
    version 12
  Zynq-7000 XC7Z020 SoC
    667 MHz
    We do not use the FPGA, and only use one core
Metrics
  Delay in cycles
    Since the victim thread should have been scheduled
  With respect to number of attack threads
    100 iterations
We observe the extent of potential HPI in seL4 on real hardware
https://www.xilinx.com/products/boards-and-kits/device-family/nav-zynq-7000.html

## Slide 14: Results: Traditional Interference
Traditional interference grows linearly with respect to the number of malicious threads
Linear with respect to number of malicious threads
Linear with respect to the server’s workload
Amount of attacker-caused HPI
Number of attacker threads allowed to start
Very small standard of deviation
Notes: Give background on the graph before the take aways

## Slide 15: Results: Thundering Herd Attacks
HPI from the Thundering Herd attacks also grows linearly
(a) Endpoint Queue Sorting Attack
(b) Replenishment Queue Sorting Attack
(c) Replenishment Wakeup Processing Attack
Linear with respect to number of attacker threads
Sorting is ~1/10th traditional HPI, but still non-trivial
Replenishment wakeup processing causes massive amounts of HPI

## Slide 16: Mitigation Strategies
System Provisioning
  Use our results to guide an admission control test
    Based on the potential HPI per-attacker, perform more complex admission control
  Effectiveness:
    For long periods of suspension, HRT schedulability is reasonable
    For short periods, HRT schedulability is challenging for the Endpoint and Replenishment Sorting attacks
    For short periods, HRT schedulability is impossible for the Replenishment Wakeup attack
Logarithmic in-kernel data structures
  Insert complexity becomes O(log(n))
    With respect to the number of attacker threads
  Effectiveness:
    Reduces HPI of Endpoint and Replenishment Sorting attacks
    No effect (slightly increases!) on the Replenishment Wakeup attack
The studied mitigation strategies have a range of effecitiveness
See the paper for a quantitative evaluation of these two strategies
Notes: Quicker here
Maybe move all the mitigation into 1 or 2 slides like this one

## Slide 17: Other Mitigation Strategies
Queue-per-priority
  Use a constant time in-kernel data structure
    Similar to a plist in Linux
  Effectiveness:
    Eliminates the Endpoint Queue Sorting attack
    Requires kernel-wide modifications for the Replenishment Wakeup Processing attack
    No effect on the Replenishment Sorting attack
Preemption points
  Capture a kernel in-progress
    Allow later kernel execution from this point
  Effectiveness:
    Bounds the cost of wait-queue and replenishment operations
    Increases kernel complexity in an undesirable way
seL4 modifications could also facilitate future mitigations
Notes: Quicker here
Maybe move all the mitigation into 1 or 2 slides like this one

## Slide 18: Mitigation Summary
No one mitigation strategy can solve all Thundering Herd attacks
 | System Provisioning | Logarithmic Data Structures | Queue-per-priority | Preemption Points
Endpoint Queue Sorting Attack |  |  |  | 
Replenishment Queue Sorting Attack |  |  |  | 
Replenishment Wakeup Processing Attack |  |  |  | 

## Slide 19: Conclusions
Investigated the system coordination dilemma
  Interference from simple IPC mechanisms
  Interference from kernel accounting mechanisms
Introduced Thundering Herd Attacks
  Non-preemptive kernel processing may delay HRT tasks
Quantified various forms of HPI
  Traditional IPC interference
  Thundering Herd Attacks
Evaluated various forms of mitigation
  No one size fits all solution!
Without careful system provisioning, kernel HPI can delay HRT tasks

## Slide 20: Questions?
Samuel Mergendahl
samuel.mergendahl@ll.mit.edu
Notes: Q&A
Notes:
Get to system c dilemma quicker
10 min over
Go over a subset of each of the attacks?